## Slide 1
61st APAC DGCA CONFERENCE · KUALA LUMPUR, MALAYSIA · 2026
Agenda Item 4 — Air Navigation
Building Navigation Resilience Against GNSS RFI
Detection, mitigation and Minimum Operational Networks across an archipelagic sky
Presented by Indonesia · AirNav Indonesia (Perum LPPNPI)
Theme: Smart Skies — Emerging Technologies for Safe, Secure, Sustainable and Efficient Aviation

## Slide 2
THE MANDATE
Responding to Action Items 60/23 and 60/18
GNSS Radio Frequency Interference — jamming (signal denial) and spoofing (position deception) — is one of the most significant emerging threats to civil aviation navigation. A single source can affect many aircraft across wide areas and cross FIR boundaries, making the threat inherently regional.
Action Item 60/23 urged States to implement detection and mitigation, share events and best practices, and ensure Minimum Operational Networks and multi-layered resilience. Indonesia manages the Jakarta and Makassar FIRs across a vast archipelagic and oceanic airspace, and has established procedures and coordination to preserve safe operations.
ACTION ITEM 60/23
"… implement GNSS RFI detection and mitigation systems … formulate and implement strategies ensuring Minimum Operational Networks (MONs) and invest in multi-layered navigational resilience." — APAC DGCA60

## Slide 3
DEFENCE IN DEPTH
Four layers of resilience
1
Detection
Procedures aligned to ICAO, applied across all ATS units. Controllers recognise position/surveillance discrepancies; pilots report cockpit anomalies; every event is documented. Low-cost, immediately deployable, highly transferable.
2
Minimum Operational Network
GNSS is never a single point of failure. On detection, controllers apply radar vectoring and transition to conventional aids — VOR, DME, ILS. A rationalised MON is a deliberate resilience investment, not a legacy cost.
3
Spectrum coordination
RFI is also a spectrum problem. AirNav coordinates with the national regulator through the Balmon spectrum monitoring centre for geolocation, tracking and enforcement against interference sources.
4
Regional sharing
Because interference crosses borders, no State acts alone. Indonesia supports the APAC GNSS/Datalink Disruption Ad Hoc Group, timely event sharing and harmonised reporting so regional data is comparable and actionable.

## Slide 4
ACTION BY THE CONFERENCE
The Conference is invited to:
a
note Indonesia’s experience detecting and mitigating GNSS RFI and maintaining multi-layered resilience across its FIRs;
b
encourage layered detection — controller training, independent surveillance and structured pilot/ATC reporting;
c
encourage retaining a rationalised MON of conventional aids (VOR/DME/ILS) and collaborating on coverage toward a regional MON;
d
encourage a formal ANSP–spectrum-authority coordination mechanism for geolocation and enforcement; and
e
urge active participation in the APAC GNSS/Datalink Disruption Ad Hoc Group with harmonised RFI event reporting.

## Slide 5
Resilience is built by layering — trained detection, a maintained MON, a bridge to spectrum authorities, and regional sharing. Indonesia has implemented all four.
Terima kasih · Thank you
AirNav Indonesia · 61st APAC DGCA Conference, Kuala Lumpur 2026